Chapter 13 Objectives:

- Explain how sound waves are produced.

- Relate frequency to pitch.

- Compare the speed of sound in various media.

- Relate plane waves to spherical waves.

- Recognize the Doppler effect and determine the direction of a frequency shift when there is relative motion between a source and an observer.

- Calculate the intensity of sound waves.

- Relate intensity, decibel level, and perceived loudness.

- Explain why resonance occurs.

- Differentiate between the harmonic series of open and closed pipes.

- Calculate the harmonics of a vibrating string and of open and closed pipes.

- Relate harmonics and timbre.

- Relate the frequency difference between two waves to the number of beats heard per second.

Chapter 13 Key Ideas

- The frequency of a sound wave determines its pitch.

- The speed of sound depends on the medium.

- The relative motion between the source of waves and an observer creates an apparent frequency shift known as the Doppler effect.

- The sound intensity of a spherical wave is the power per area: Intensity=P/(4πr2)

- Decibel level is relative intensity.

- A forced vibration at the natural frequency produces resonance.

- Harmonics of a vibrating string or a pipe open at both ends can be found with the equation: fn= n(v/2L), with n=1,2,3,….

- Harmonics of a pipe closed at one end can be found with the equation: fn=n(v/4L)

- The number and intensity of harmonics account for the sound quality of an instrument, also known as timbre.

Key Terms

Beat, compression, decibel level, Doppler effect, fundamental frequency, harmonic series, intensity, pitch, rarefaction, resonance, timbre